CECivil Engineering: Gate 2007 Paper

GATE: 2007

CE: CIVIL ENGINEERING

Q.1 – Q.20 Carry One Mark Each

1 1 3

	

Q.1	The minimum and the maximum eigen values of the matrix  1 5 1  are -2 and

	

6, respectively. What is the other eigen value?

3 1 1

(A) 5

(B) 3

(C) 1

2

d x

3

= 0 is

(D) -1

Q.2	The degree of the differential equation

dt

22 x

(A) 0   	(B) 1

(C) 2

dy2

(D) 3

Q.3 	The solution for the differential equation

x=0 is

dx

x y  with condition that y = 1 at

1

x

3

x

2

x

3

(A)

y e2x

y

( ) ln( )

	

4

3

y

( ) ln( )

2

d y e3

( )

Q.4 	An axially loaded bar is subjected to a normal stress of 173 MPa. The shear stress

in the bar is

(A) 75MPa

(B) 86.5MPa

(C) 100MPa

(D) 122.3MPa

Q.5 	A steel column, pinned at both ends, has a buckling load of  200kN. If the column

is restrained against lateral movement at its mid-height, its buckling load will be

(A) 200kN

(B) 283kN

(C) 400kN

(D) 800kN

Q.6 	The stiffness coefficient kij indicates

(A) force at i due to a unit deformation at j.

(B) deformation at j due to a unit force at i.

(C) deformation at i due to a unit force at j.

(D) force at j due to a unit deformation at i.

Q.7 	For an isotropic material, the relationship between the Young’s modulus (E),

shear modulus (G) and Poisson’s ratio () is given by

A G

( )



E



B E

( )



G



C G

( )



E



D G

( )



E



2(1	)

2(1	)

(1 2 )

2(1−	)

1

CECivil Engineering: Gate 2007 Paper

Q.8 	A clay soil sample is tested in triaxial apparatus in consolidated-drained

conditions at a cell pressure of 100 kN/m2. What will be the pore water pressure at

a deviator stress of 40kN/m2?

(A) 0kN /m2

(B) 20kN/m2

(C) 40kN/m2

(D) 60kN/m2

Q.9 	The number of blows observed in a Standard Penetration Test (SPT) for different

penetration depths are given as follows.

Penetration of sampler

0-150mm

150-300mm

300-450mm

The observed N value is

(A) 8   	        (B) 14

Number of blows

6

8

10

(C) 18

(D) 24

Q.10  The  vertical  stress  at  some  depth  below  the  corner  of  a  2m  x  3m  rectangular

footing  due  to  a  certain  load  intensity  is  100  kN  /  m2  below  the  centre  of  a

4m x 6m rectangular  footing at the same depth and same load intensity?

(A) 25

(B) 100

(C) 200

(D) 400

Q.11  There is a free overfall at the end of a long open channel. For a given flow rate,

the critical depth is less than the normal depth. What gradually varied flow profile

will occur in the channel for this flow rate?

(A) M1

(B) M2

(C) M3

(D) S1

Q.12  The  consumptive  use  of  water  for  a  crop  during  a  particular  stage  of  growth  is

2.0mm  /  day.  The  maximum  depth  of  available  water  is  the  root  zone  is  60mm.

Irrigation is required when the amount of available water is 50% of the maximum

available water in the root zone. Frequency of irrigation should be

(A) 10 days

(B) 15days

(C) 20days

(D) 25days

Q.13  As  per  the  Lacey’s  method  for  design  of  alluvial  channels,  identity  the  true

statement from the following

(A) Wetted perimeter increases with an increase in design discharge

(B) Hydraulic radius increases with an increase in silt factor.

(C) Wetted perimeter decreases with an increase in design discharge.

(D) Wetted perimeter increases with an increase in silt factor.

Q.14  At two points 1 and 2 in a pipeline the velocities are V and 2V, respectively. Both

the points are at the same elevation. Both the points are at the same elevation. The

2

CECivil Engineering: Gate 2007 Paper

fluid density is . The flow can be assumed to be in compressible, inviscid, steady

and irrotational. The difference in pressures P1 and P2 at points 1 and 2 is

(A) 0.5V2

(B) 1.5V2

(C) 2V2

(D) 3V2

Q.15  The presence of hardness in excess of permissible limit causes

(A) Cardio Vascular problems

(C) Calcium deficiency

(B) Skin discolouration

(D) Increased laundry expenses

Q.16  The dispersion of pollutants in atmosphere is maximum when

(A) environmental lapse rate is greater than adiabatic lapse rate.

(B) environmental lapse rate is less than adiabatic lapse rate.

(C) environmental lapse rate is equal to adiabatic lapse rate.

(D) maximum mixing depth is equal to zero.

Q.17  The alkalinity and the hardness of a water sample are 250mg/L and 350 mg/L as

CaCo3, respectively. The water has

(A) 350 mg/L carbonate hardness and zero non-carbonate hardness.

(B) 250mg/L carbonate hardness and  zero non-carbonate hardness.

(C) 250mg/L carbonate hardness and 350 mg/L non-carbonate hardness.

(D) 250mg/L carbonate hardness and 100 mg/L non-carbonate hardness.

Q.18  The consistency and flow resistance of bitumen can be determined from the

following.

(A) Ductility test

(C) Softening point Test

(B) Penetration test

(D) Viscosity test

Q.19  If a two-lane national highway and a two-lane state highway intersect at right

right angles, the number of potential conflict points at the intersection, assuming

that both the roads are two-way is

(A) 11

(B) 17

(C) 24

(D) 32

Q.20  In signal design as per Indian Roads Congress specifications, if the sum of the

ratios of normal flows to saturation flow of two directional traffic flow is 0.50 and

the total lost time per cycle is 10 seconds, the optimum cycle length in seconds is

(A) 100

(B) 80

(C) 60

(D) 40

Q.21 to Q.75 carry two marks each

Q.21  For what values of  and  the following simultaneous equations have an infinite

number of solutions?

x + y + z = 5;

x + 2y + z = 

x + 3y + 3z = 9;

(A) 2,7

(B) 3,8

(C) 8,3

(D) 7,2

3

Q.22  A velocity vector is given as

CECivil Engineering: Gate 2007 Paper

r

r

2

r

2

r

V 5xy i	2 y j 3 yz k .

The divergence of this velocity vector at (1,1,1) is

(A) 9

(B) 10

(C) 14

(D) 15

Q.23  A body originally at 600C cools down to 400C in 15minutes when kept in air at a

temperature of 250C. What will be the temperature of the body at the end of

30minutes?

(A) 35.20C

(B) 31.50C

(C) 28.70C

(D) 150C

Q.24  The following equation needs to be numerically solved using the Newton-

Raphson method.

x3 + 4x – 9 = 0

The iterative equation for this purpose is (k indicates the iteration level)

A x



2x

3 

9

B x



3x

2 

4

( )

k1

k

2 

3xk

4

( )

k1

k

2	

2xk

9

	−2



4x

2 

3

C x

( )



x

x

3

4

D x

( )



k

k	1

∞

k

sin t

k

k	1

2 

9xk

2

Q.25  Evaluate  ∫

0



( )

t

dt

( )



2

( )



4

( )



3

Q.26  Potential function  is given as

2	2

x	y	. What will be the stream function

() with the condition  = 0 at x = y = 0?

(A) 2xy

(B) x2 + y2

(C) x2 – y2

1	2

(D) 2x2y2

Q.27  The inverse of the 2 x 2 matrix  

  is

1 −7	2 

5	7

1 7	2

( )

	

( )





3  5

−1

3 5	1

( )

1  7	−2

	

( )

1 −7	−2

	

3 −5	1 

3 −5	−1

Q.28  Given that one root of the equation x3-10x2+31x-30=0 is 5, the other two roots are

(A) 2 and 3

(B) 2 and 4

(C) 3 and 4

(D) -2 and -3

4

CECivil Engineering: Gate 2007 Paper

Q.29  If the standard deviation of the spot speed of vehicles in a highway is 8.8 kmph

and the mean speed of the vehicles is 33kmph, the coefficient of variation in

speed is

(A) 0.1517

(B) 0.1867

(C) 0.2666

(D) 0.3646

Q.30  A metal bar of length 100mm is inserted between two rigid supports and its

temperature is increased by 100C. If the coefficient of thermal expansion is 12 x

10-6 per 0C and the Young’s modulus is 2 x 105 MPa, the stress in the bar is

(A) zero

(B) 12MPa

(C) 24MPa

(D) 2400MPa

Q.31  A rigid bar is suspended by three rods made of the same material as shown in the

figure. The area and length of the central rod are 3A and L, respectively while that

of the two outer rods are 2A and 2L respectively. If a downward force of 50kN is

applied to the rigid bar, the forces in the central and each of the outer rods will be

(A) 16.67 kN each

(C) 30kN and 10kN

(B) 30kN and 15kN

(D) 21.4kN and 14.3kN

Q.32  The maximum and minimum shear stresses in a hollow circular shaft of outer

diameter 20mm and thickness 2mm, subjected to a torque of 92.7 N.m will be

(A) 59 MPa and 47.2 MPa

(C) 118 MPa and 160 MPa

(B) 10MPa and 80MPa

(D) 200 MPa and 160 MPa

Q.33  The shear stress at the neutral axis in a beam of triangular section with a base of

40mm and height of 20mm, subjected to a shear force of 3kN is

(A) 3MPa

(B) 6MPa

(C) 10MPa

(D) 20MPa

Q.34  U1 and U2 are the strain energies stored in a prismatic bar due to axial tensile

forces P1 and P2 respectively. The strain energy stored in the same bar due to

combined action of P1 and P2 will be

(A) U = U1 + U2

(C) U <U1 + U2

(B) U = U1 U2

(D) U >1 + U2

Q.35  The right triangular truss is made of members having equal cross sectional area of

1550 mm2 and Young’s modulus of 2 x 105 MPa. The horizontal deflection of the

joint Q is

Q

135kN

6m

P

4.5m

R

(A) 2.47mm

(B) 10.25mm

(C) 14.1mm

(D) 15.68mm

5

CECivil Engineering: Gate 2007 Paper

Q.36  The influence line diagram (ILD) shown is for the member

compression

P

R

Q

S

ILD

tension

(A) PS

(B) RS

(C) PQ

(D) QS

Q.37  Consider the following statements:

1.

2.

3.

The compressive strength of concrete decreases with increase in water-

cement ratio of the concrete mix.

Water is added to the concrete mix for hydration of cement and

workability.

Creep and shrinkage of concrete are independent of the water-cement ratio

in the concrete mix.

The true statements are

(A) 1 and 2 	(B) 1, 2 and 3

(C) 2 and 3

(D) only 2

Q.38  The percentage loss of prestress due to anchorage slip of 3mm in a concrete beam

of length 30m which is post-tensioned by a tendon with an initial stress of 1200 N

/ mm2 and modulus of elasticity equal to 2.1 x 105 N/mm2 is

(A) 0.0175

(B) 0.175

(C) 1.75

(D) 17.5

Q.39  A concrete beam of rectangular cross-section of size 120mm (width) and 200mm

(depth) is prestressed by a straight tendon to an effective force of 150kN at an

eccentricity of 20mm (below the centroidal axis in the depth direction). The

stresses at the top and bottom fibres of the section are

(A) 2.5 N/mm2 (compression), 10N/mm2 (compression)

(B) 10N / mm2 (tension), 3.75 N / mm2

(C) 3.75 N/mm2 (tension), 3.75 N/mm2 (compression)

(D) 2.75 N/mm2 (compression), 3.75 N/mm2 (compression)

Q.40  Consider the following statements:

I.	Modulus of elasticity concrete increases with increase in compressive

strength of concrete.

II.	Brittleness of concrete increases with decrease in compressive strength of

concrete.

6

CECivil Engineering: Gate 2007 Paper

III.	Shear strength of concrete increases with increase in compressive strength

of concrete.

The TRUE statements are

(A) II and III

(B) I, II and III

(C) I and II

(D) I and III

Q.41  A steel flat of rectangular section of size 70 x 6 mm is connected to a gusset plate

by three bolts each having a shear capacity of 15kN in holes having diameter

11.5mm. If the allowable tensile stress in the flat is 150MPa, the maximum

tension that can be applied to the flat is

15

T

(A) 42.3kN

35

20

20

15

(B) 52.65kN

(C) 59.5kN

(D) 63.0kN

Q.42  A bracket connection is made with four bolts of 10mm diameter and supports a

load of 10kN a an eccentricity of 100mm. the maximum force to be resisted by

any bolt will be

P 10kN

30

30

40 40

(A) 5kN

(B) 6.5kN

(C) 6.8kN

(D) 7.16kN

Q.43  The plastic collapse load Wp for the propped cantilever supporting two point loads

as shown in the figure in terms of plastic moment capacity, Mp is given by

L/3

W

L/3

W

L/3

(A) 3Mp/L

(B) 4Mp/L

(C) 5 Mp/L

(D) 6Mp/L

7

CECivil Engineering: Gate 2007 Paper

Q.44  Sieve analysis on a dry soil sample of mass 1000g showed that 980g and 270g of

soil pass through 4.75mm and 0.075mm sieve, respectively. The liquid limit and

plastic limits of the soil fraction passing through 425 sieves are 40% and 18%

respectively. The soil may be classified as

(A) SC

(B) MI

(C) CI

(D) SM

Q.45  The water content of a saturated soil and the specific gravity of soil solids were

found to be 30% and 2.70, respectively. Assuming the unit weight of water to be

10kN / m3, the saturated unit weight (kN/m3), and the void ratio of the soil are

(A) 19.4, 0.81

(B) 18.5, 0.30

(C) 19.4. 0.45

(D) 18.5, 0.45

Q.46  The factor of safety of an infinite soil slope shown in the figure having the

c





0	



3

kN m and





3

kN m

is

properties c=0,

0,	35 ,

dry

16	/

sat

20	/

approximately equal to

10m8m

300

(A) 0.70

(B) 0.80

(C) 1.00

(D) 1.20

Q.47  Match the following groups

Group – I

P 	Constant head permeability test

Q 	Consolidation test

R 	Pycnometer test

S 	Negative skin friction

Group – II

1. 	Pile foundations

2. 	Specific gravity

3. 	Clay soil

4. 	Sand

(A) P-4, Q-3, R-2, S-1

(C) P-3, Q-4, R-2, S-1

(B) P-4, Q-2, R-3, S-1

(D) P-4, Q-1, R-2, S-3

8

CECivil Engineering: Gate 2007 Paper

Q.48  The bearing capacity of a rectangular footing of plan dimensions 1.5m x 3m

resting on the surface of a sand deposit was estimated as 600 kN/m2 when the

water table is far below the base of the footing. The bearing capacities in kN/m2

when the water level rises to depths of 3m, 1.5m and 0.5m below the base of the

footing are

(A) 600, 600, 400

(C) 600, 500, 250

(B) 600, 450, 350

(D) 600, 400, 250

Q.49  What is the ultimate capacity in kN of the pile group shown in the figure

assuming the group to fail as a single block?

0.4m diameter piles

10m

1.2m c/c

1.2m c/c

Clay soil

C   = 40kN/m2

(A) 921.6

(B) 1177.6

(C) 2438.6

(D) 3481.6

Q.50  A horizontal water jet with a velocity of 10m/s and cross sectional area of 10mm2

strikes a flat plate held normal to the flow direction. The density of water is 1000

kg/m3. The total force on the plate due to the jet is

(A) 100N

(B) 10N

(C) 1N

(D) 0.1N

Q.51  A 1:50 scale model of a spillway is to be tested in the laboratory. The discharge in

the prototype is 1000M3 /s. The discharge to be maintained in the model test is

(A) 0.057m3/s

(B) 0.08m2/s

(C) 0.57m3/s

(D) 5.7m3/s

Q.52  A triangular open channel has a vertex angle of 900 and carries flow at a critical

depth of 0.30m. the discharge in the channel is

(A) 0.08m3/s

(B) 0.11 m3/s

(C) 0.15 m3/s

(D) 0.2 m3/s

Q.53  Flow rate of a fluid (density = 1000kg/m3) in a small diameter tube is 800 m3/s.

The length and the diameter of the tube are 2m and 0.5mm, respectively. The

pressure drop in 2m length is equal to 2.0MPa. The viscosity of the fluid is

(A) 0.025N.s/m2

(B) 0.012N.s/m2

(C) 0.0092 N.s/m2(D) 0.00102 N.s/m2

9

CECivil Engineering: Gate 2007 Paper

Q.54  The flow rate in a wide rectangular open channel is 2.0m3/s per meter width. The

channel bed slope is 0.002. The Manning’s roughness coefficient is 0.012. The

slope of the channel is classified as

(A) Critical

(B) Horizontal

(C) Mild

(D) Steep

Q.55  The culturable command area for a distributary channel is 20,000 hectares. Wheat

grown in the entire area and the intensity of irrigation is 50%. The kor period for

wheat is 30 days and the kor water depth is 120mm. The outlet discharge for the

distributary should be

(A) 2.85m3/s

(B) 3.21m3/s

(C) 4.63m3/s

(D) 5.23m3/s

Q.56  An isolated 4-hour storm occurred over a catchment as follows

Time

Rainfall (mm)

1st hour

9

2nd hour

28

3rd hour

12

4th hour

7

The  index for the catchment is 10mm/h. The estimated runoff depth from the

catchment due to the above storm is

(A) 10mm

(B) 16mm

(C) 20mm

(D) 23mm

Q.57  Two electrostatic precipitators (ESPs) are in series. The fractional efficiencies of

the upstream and downstream ESPs for size dp are 80% and 65%. Respectively.

What is the overall efficiency of the system for the same dp?

(A) 100%

(B) 93%

(C) 80%

(D) 65%

Q.58  50g of CO2 and 25g of CH4 are produced from the decomposition of municipal

solid waste (MSW) with a formula weight of 120g. What is the average per capita

green house gas production in a city of 1 million people with a MSW production

rate of 500 ton / day?

(A) 104 g/day

(B) 120 g/day

(C) 208 g/day

(D) 313 g /day

Q.59  The extra widening required for a two-lane national highway at a horizontal curve

of 300 m radius, considering a wheel base of 8m and a design speed of 100kmph

is

(A) 0.42m

(B) 0.62m

(C) 0.82m

(D) 0.92m

Q.60  While designing a hill road with a ruling gradient of 6%, if a sharp horizontal

curve of 50m radius is encountered, the compensated gradient at the curve as per

the Indian Roads Congress specifications should be

(A) 4.4%

(B) 4.75%

(C) 5.0%

(D) 5.25%

10

CECivil Engineering: Gate 2007 Paper

Q.61  The design speed on a road is 60kmph. Assuming the driver reaction time of 2.5

seconds and coefficient of friction of pavement surface as 0.35, the required

stopped distance for two-way traffic on a single lane road is

(A) 82.1m

(B) 102.4

(C) 164.2m

(D) 186.4m

Q.62  The width of the expansion joint is 20mm in a cement concrete pavement. The

laying temperature is 200C and the maximum slab temperature in summer is 600C.

The coefficient of thermal expansion of concrete is 10 x 10-6 mm/mm / 0C and the

joint filler compresses upto 50% of the thickness. The spacing between expansion

joints should be

(A) 20m

(B) 25m

(C) 30m

(D) 40m

Q.63  The following data pertains to the number of commercial vehicles per day for the

design of a flexible pavement for a national highway as per IRC: 37-1984

Type of commercial Number of vehicles per day

Vehicle Damage Factor

vehicle considering the number of lanes

Two axle trucks

2000  5

Tandem axle trucks  200 	6

Assuming a traffic growth factor of 7.5% per annum for both the types of

vehicles, the cumulative number of standard axle load repetitions (in million) for

a design life of ten years is

(A) 44.6

(B) 57.8

(C) 62.4

(D) 78.7

Q.64  Match the following tests on aggregate and its properties

P.

Q.

R.

S.

TEST

Crushing Test

Los Angles abrasion test

Soundness test

Angularity test

1.

2.

3.

4.

PROPERTY

Hardness

Weathering

Shape

Strength

(A) P-2, Q-1, R-4, S-3

(C) P-3, Q-2, R-1, S-4

(B) P-4, Q-2, R-3, S-1

(D) P-4, Q-1, R-2, S-2

Q.65  The plan of a map was photo copied to a reduced size such that a line originally

100mm, measures 90mm. The original scale of the plan was 1:1000. The revised

scale is

(A) 1:900

(B) 1:11111

(C) 1:1121

(D) 1:1221

11

CECivil Engineering: Gate 2007 Paper

Q.66  The following table gives data of consecutive coordinates in respect of a closed

theodolite traverse PQRSP.

P

Q

R

S

Station

Northing, m

400.75

100.25

Southing, m

199.0

300.0

Easting, m 	Westing, m

300.5

199.25

399.75

200.5

The magnitude and direction of error of closure in whole circle bearing are

(A) 2.0m and 450

(C) 2.82m and 3150

(B) 2.0m and 3150

(D) 3.42m and 450

Q.67  The following measurements were made during testing a leveling instrument.

Staff Reading at

Instrument at

P

Q

P1

2.800m

2.700m

Q1

1.700m

1.800m

P1 is close to P and Q1 is close to Q. If the reduced level of station P is 100.000m,

the reduced level of station Q is

(A) 99.000m

(B) 100.000m

(C) 101.000m

(D) 102.000m

Q.68  Two straight lines intersect at an angle of 600. The radius of a curve joining the

two straight lines is 600m. The length of long chord and mid-ordinates in metres

of the curve are

(A) 80.4, 600.00

(B) 600.0, 80.4

(C) 600.0, 39.89

(D) 40, 89,300

Q.69  The magnetic bearing of a line AB is S 450 E and the declination is 50 West. The

true bearing of the line AB is

(A) S 450 E

(B) S 400 E

(C) S 500 E

(D) S 500 W

COMMON DATA QUESTIONS

Common Data for Questions 70 and 71

Water is flowing through the permeability apparatus as shown in the figure. The

coefficient of permeability of the soil is km/s and the porosity of the soil sample is

0.50.

12

soil

R

0.4m

0.8m

0.4m

CECivil Engineering: Gate 2007 Paper

Q.70  The total head, elevation head and pressure head in metres of water at the point R

shown in the figure are

(A) 0.8, 0.4, 0.4

(C) 0.4, 0, 0.4

(B) 1.2, 0.4, 0.8

(D) 1.6, 0.4, 1.2

Q.71  What are the discharge velocity and seepage velocity through the soil sample?

(A) k, 2k

(B) 2/3k, 4/3k

(C) 2k,k

(D) 4/3k, 2/3k

Common Data for Questions 72 and 73:

Ordinates of a 1-hour unit hydrograph at 1 hour intervals, starting from time t = 0,

are 0, 2, 6,4,2,1 and 0 m3/s.

Q.72  Catchment area represented by this unit hydrograph is

(A) 1.0 km2

(B) 2.0 km2

(C) 3.2 km2

(D) 5.4 km2

Q.73  Ordinate of a 3-hour unit hydrograph for the catchment at t=3 hours is

(A) 2.0m3/s

(B) 3.0m3/s

(C) 4.0m3/s

(D) 5.0m3/s

Common Data for Questions 74 and 75:

A completely mixed activated sludge process is used to treat a wastewater flow of

1  million  litres  per  day  (1  MLD)  having  a  BOD5  of  200  mg/L.  The  biomass

concentration in the aeration tank is 2000 mg/L and the concentration of the net

biomass leaving the system of 50mg/L. the aeration tank has a volume of 200 m3.

Q.74  What is the hydraulic retention time of the wastewater in aeration tank?

(A) 0.2h

(B) 4.8h

(C) 10h

(D) 24h

13

CECivil Engineering: Gate 2007 Paper

Q.75  What is the average time for which the biomass stays in the system?

(A) 5h

(B) 8h

(C) 2days

(D) 8 days

Linked Answer Questions: Q.76 to Q.85 carry TWO marks each

Statement for Linked Answer Questions 76 and 77

A two span continuous beam having equal spans each of length L is subjected to a

uniformly  distributed  load    per  unit  length.  The  beam  has  constant  flexural

rigidity.

Q.76  The reaction at the middle support is

L

L

L2

(A) L

(B) 5

2

(C) 5

4

(D)

16

Statement for Linked Answer Questions 78 and 79

A  singly  reinforced  rectangular  concrete  beam  has  a  width  of  150mm  and  an  effective

depth of 330mm. The characteristic compressive strength of concrete is 20 MPa. Adopt

the stress block for concrete as given in IS 456-2000 and take limiting value of depth of

neutral axis as 0.48 times the effective depth of the beam.

Q.78  The limiting value of the moment of resistance of the beam is kN.m is

(A) 0.14

(B) 0.45

(C) 45.08

(D) 156.82

Q.79  The limiting area of tension steel in mm2 is

(A) 473.9 	(B) 412.3 	(C) 373.9

Statement for Linked Answer Questions 80 and 81

(D) 312.3

The ground conditions at a site are as shown in the figure. The water table at the

site which was initially at a depth of 5m below the ground level got permanently

lowered to a depth of 15m below the ground level due to pumping of water over a

few years. Assume the following data

i.	unit weight of water = 10kN/m3

ii.	unit weight of sand above water table = 18kN/m3

iii.	unit weight of sand and clay below the water table = 20kN/m3

iv.	coefficient of volume compressibility = 0.25m2/MN

G.L.

5m

original water table

15m

20m

lowered water table

5m

Clay soil

5m

14

CECivil Engineering: Gate 2007 Paper

Q.80  What is the change in the effective stress in kN/m2 at mid-depth of the clay layer

due to the lowering of the water table?

(A) 0

(B) 20

(C) 80

(D) 100

Q.81  What is the compression of the clay layer in mm due to the lowering of the water

table?

(A) 125

(B) 100

(C) 25

(D) 0

Statement for Linked Answer Questions 82 and 83

A rectangular open channel needs to be designed to carry a flow of 2.0m3/s under

uniform  flow  conditions.  The  Manning’s  roughness  coefficient  is  0.018.  The

channel  should  be  such  that  the  flow  depth  is  equal  to  half  the  width,  and  the

Froude number is equal to 0.5.

Q.82  The bed slope of the channel to be provided is

(A) 0.0012

(B) 0.0021

(C) 0.0025

(D) 0.0052

Q.83  Keeping  the  width,  flow  depth  and  roughness  the  same,  if  the  bed  slope  of  the

above channel is doubled, the average, boundary shear stress under uniform flow

conditions is

(A) 5.6 N/m2

(B) 10.8 N/m2

(C) 12.3 N/m2

(D) 17.2 N/m2

Statement for Linked Answer Questions 84 and 85

A plain sedimentation tank with a length of 20m, width of 10m, and a depth of 3m

is  used  in  a  water  treatment  plant  to  treat  4  million  litres  of  water  per  day  (4

MLD). The average temperature of water is 200C. The dynamic viscosity of water

is 1.002 x 10-3 N.s/m2 at 200 C. Density of water is 998.2 kg/M3. Average specific

gravity of particles is 2.65.

Q.84  What is the surface overflow rate in the sedimentation tank?

(A) 20m3 / m2 / day

(C) 67m3 / m2 / day

(B) 40m3 / m2 / day

(D) 133m3 / m2 / day

Q.85  What is the minimum diameter of the particle which can be removed with 100%

efficiency in the above sedimentation tank?

(A) 11.8 x 10-3 mm

(C) 50 x 10-3 mm

(B) 16.0 x 10-3 mm

(D) 160 x 10-3 mm

15