ATMIYA INSTITUTE OF TECHNOLOGY & SCIENCE

EC DEPARTMENT

Optical Communication

Model Paper-I							Marks: 30

Section I

1. A material with Band Gap energy of 1.2 eV is used in photon emission. Find the frequency and wavelength of emitted light?						[2]

2. Explain stimulated emission with the help of diagram.				[3]

3. Draw a neat labeled sketch of Surface Edge Emitting LED and explain.		[4]

4.  What is the difference between Optical and Electrical bandwidth? 		[3]

5. Compare the properties of multimode and single mode Lasers. 			[3]

Section II

6.  Explain the following terms with diagrams:                                                        	 [3]

Reflection and Refraction.

7.  Explain: Acceptance angle and critical angle.                                                    	 [3]

8.  Explain: Step index fiber and Graded index fiber with refractive index profile.   [3]

9.  Explain OVPO method for fiber fabrication.                                                    	  [3]

10.  A silica optical fiber with a core diameter large enough to be considered by ray

theory analysis has a core refractive index of 1.5 and a cladding refractive index

of 1.47. Determine 	(a) the critical angle at the core-cladding interface,

(b) the NA for the fiber,

(c) the acceptance angle in air for the fiber.		[3]

ATMIYA INSTITUTE OF TECHNOLOGY & SCIENCE

EC DEPARTMENT

Optical Communication

Model Paper-II							Marks: 30

Section I

1. A typical LED emits light at λ =0.82μm and ∆λ= 40μm.

Find i) relative line width in percent      and ii).  Band width (∆f)		[2]

2. Why Hetrojunction structure is used in Optical Sources? Draw the diagram of a double

hetrojunction structure of LED .							[3]

3. What are the properties of light sources used for optical communications? Compare

the features of LED & LASER.							[5]

4. Draw a neat labeled sketch of Edge Emitting LED.				[2]

5. List out the features Fabry –Perot Resonator cavity for Laser diodes.		[3]

Section II

6.  Explain MCVD  for fiber fabrication.                                                                  	 [3]

7.  Explain characteristics of fiber cables.                                                                 	 [3]

8.  Explain indoor and outdoor cable design with diagram.                                      	 [3]

9.  What is the advantage of optical fibers compared to copper wires?                     	 [3]

10.  A graded index fiber has a core with a parabolic refractive index profile which has a

diameter of 50 μm. The fiber has a numerical aperture of 0.2. Estimate the total

number of guided modes propagating in the fiber when it is operating at a

wavelength  of 1 μm.                                                                                            [3]